## Slide 1: IMSI Catchers in 5G
RAlice

## Slide 2: IMSI Catchers
Radio frontend
Network backend
Attacks:
Battery drain
DoS
Downgrading to a lower generation network
Passive:
Less powerful
Difficult to detect
Active:
More powerful
Can control mobile devices

## Slide 3: 5G – More secure against IMSI Catchers?
IMSI/SUPI is never disclosed in clear when a mobile device is establishing a connection.
5G uses only a temporary paging identifier that must be refreshed after each use.
If an attacker intercepts the SUCI the information is useless and cannot be used to harvest data.
Mechanism to defend against IMSI Catchers
During a call/data transaction a mobile phone sends measurement reports to the network.
The core network can use that information to try to identify fake towers.
Operators can implement these features and mechanisms.

## Slide 4: Device capabilities
When the mobile device communicates its capabilities to the core network, there can be misconfigurations in the network.
Man in the middle can modify these capabilities and attack or downgrade the user to a less secure network.
In 5G the capability should only be exchanged after having established a secure session.

## Slide 5: Other threats
Poor carrier implementation: that would allow IMSI catchers to operate as usual.
SUCI reveals some information
https://i.blackhat.com/USA21/Wednesday-Handouts/us-21-5G-IMSI-Catchers-Mirage.pdf
Lack of mandatory regulations to frequently update the random identifiers.

## Slide 6: Conclusion
End users have no control over choosing the most secure network.
SUCI decoding leads to identification of roaming subscribers.
IMSI Catcher attack is possible in 5G NSA and SA.

## Slide 7: Resources
https://www.securitymagazine.com/articles/91767-protecting-high-level-personnel-from-imsi-catchers
https://www.thalesgroup.com/en/worldwide-digital-identity-and-security/mobile/magazine/5g-sim-security-and-privacy-imsis
https://www.sciencedirect.com/science/article/abs/pii/S1389128621002061
https://i.blackhat.com/USA21/Wednesday-Handouts/us-21-5G-IMSI-Catchers-Mirage.pdf

## Slide 8: Thank you!